## Slide 1: Scan of GEMs with FIT 10cm radial zigzag readout boards at BNL
Aiwu Zhang
2015-08-31

## Slide 2: Setup
120°
0.05 mm collimator
Length 8 mm
h
r
Beam spot size d=70~80 um.
Detector gas gaps: 5.63/1.34/1.54/1.53 mm, gas was Ar/CO2 70:30.
X ray collimator: 0.05 mm by 8 mm, and was a few mm above drift. Correspondingly, beam spot is estimated to 70-80 um.
For each FIT board (with 30 or 48 zigzag strips), 3 rows (small, middle, large R) were scanned, in each row 100 runs were taken with 0.1 mm step. (10 mm range was scanned, not sure if absolute position was noted down).
Fields (in gaps): 1, 3, 3, 3 kV/cm; voltage across GEM : 332V for low gain (only for last 30 runs for ZZ_30_largeR), voltage unknown for high gain.
Small R
Middle R
Large R

## Slide 3
77.12
78.65
3.75
7.11
origin
X
Y
15
55
9.9
Small R scans
in –X direction
50
85
Middle R scans
in –X direction
Large R scans
in –X direction
Unit in mm
Based on 48-strip board,
similar for 30-strip board.
Due to Altium resolution, the zigzag shape is not shown correctly, please ignore.

## Slide 4: Fraction of cluster multiplicity = 1 events (ZZ_30). Most of runs have <20% of clusterMult=1 events.
Small R scan
Middle R scan
Large R scan
Fraction of cluster size = 1 events in all clusterMulti = 1 events.
Lower
gain runs

## Slide 5: Example of some raw signals (after threshold cut, ZZ30_smallR_run80007, clusterMult=1)
Note that maximum charge happens in different time bins for different strip numbers. How do we define total/strip charge in a cluster? (since charge is needed when calculating centroid (hit) positions.)

## Slide 6: Mean and Sigma of Position Distributions (ZZ30, clusterMult=1)
Charge is defined from integration of each strip in a cluster (get similar results if peak charge is used).
A bad thing: at some x ray positions, measured position does not change. This insensitivity is not due to single-strip clusters .
A good thing: for those positions, widths of position distributions are very small (<30 urad).

## Slide 7: Measured Positions vs. X ray Positions (in ϕ, ZZ30, clusterMult=1)
Red lines are fitted profiles, purple lines are perfect relations one expects.
The distance between the red line and purple line indicates an offset of ~2 strips;
The slopes of these fitted lines are not equal to 1, meaning that there are rotations need to be corrected.
Small R
Middle R
Large R

## Slide 8: Mean and Sigma of Residual (=Centroid-xRayPos) Distributions (in ϕ coordinate, ZZ30, clusterMult=1)
X ray position for each run is estimated. Consider 50 um collimator and a few mm between source and drift, beam spot is estimated to be 70 um.
In order to get a “track”, X ray position is smeared with a Gaussian function with sigma 70um/R (done in ϕ coordinate).
Then residual can be calculated as usual from .
Mean residual can be tuned to 0 by proper alignment. But the point here is that mean residual vs. X ray position shows the “radial” zigzag structure.
Also, residual widths are shown on the bottom.

## Slide 9: Residual vs. X ray pos. (in ϕ coordinate, ZZ30, clusterMult=1)
Small R
Middle R
Large R

## Slide 10: Residual vs. η. (correction function, ZZ30, clusterMult=1)
Small R
Middle R
Large R
is the quantity that was used for beam test data correction.
And, correction functions were found by looking at (exclusive) residual vs. η.
Here, similar (residual vs. η) plots were produced for all >1 strip multiplicities events.

## Slide 11: Residual vs. η. (correction function fitted, ZZ30, clusterMult=1)
Small R
Middle R
Large R
Plots were fitted using polynomial functions, as a first try, these functions don’t help “flatting” the residual vs. η plots.

## Slide 12: Summary
Have got preliminary understanding on the scans of FIT zigzag boards.
Number of good events (clusterMulti=1) are few (<20%) for most of runs (w/ 5k events per run); also it makes difficult to separate events by strip-multiplicities.
Correction functions were made, but need to refine to get better results.

## Slide 13
X
ZZ48_smallR: startPoint (X) and endPoint (O), across 5 strips.
O
Back up